# TO DO

+ ram arrays declaration and multiple assignation!

return must exit function and ¿¿¿ l2gr check ???

- convert wl wr to udp2 and disable old F100 and F000 instructions
- Do get timer count y timer repeats

+ delay

- Rhino Tuna, all instruction names and comments text compression/decompression

# About cF
### Pre history of cF
Prehistoria de cF, el sueño de construir un robot me ha inquietado desde que recuerdo.
Definamos el concepto, quería construir una mezcla entre R2-D2, y un rover lunar de la nasa capaz de campar y vivir a sus anchas en los desiertos de forteventura, de manera autosuficiente, reportando datos y ejecutando acciones. Y darle también una ligera IA y capacidad de hablar.

Comenzé el proyecto mil y una veces en mi adolescencia, y obtuve mil y un fracasos.
Tras graduarme en Electrónica comenzé con el proyecto seriamente, pero avanza de forma muy lenta ya que su propio desarrollo ha dado pié a proyectos que lo sobrepasa en cuanto a utilidades prácticas y complejidad se refiere.
Entienda el lector el carácter de prólogo de los presentes párrafos ya que, pese que AL-1 sea el principal sujeto de pruebas y experimentos, no es lo que pretendo presentar.

En un comienzo se pensaba utilizar una frecuencia pública (legal), para comunicar con el robot, con el fin de controlarlo a distancias de decenas de kilómetros.
Idea que, fue descartada al mirar el calendario y advertir que era ya 2016. Entonces se pensó en la WWW.

Todos los filtros pasa banda diseñados en proteus fueron directamente a la papelera de reciclaje, la pizarra fué borrada y se dio lo que el escritor llama, el primer re-enfoque del proyecto.

Me di cuenta de que lo que quería era un automata,barato, y eficiente trabajando con un mini-ordenador que almacenase la IA.
Podía hacerlo todo en Python con una raspberry pi y olvidarme.
¿Todo? Todo no. Yo quería muchos canales Analógicos, modulacion por ancho de pulso, infrarójos, ultrasonidos, “infinitas” entradas y salidas digitales para controlar circuitos de potencia, que tuviera Ip fija, que fuera un punto de acceso, que comunicase o consultase cualquier dato en red, motores paso a paso para múltiples articulaciones.

De modo que opté por almacenar la IA en un pic32 o raspberry (reconocer voz y hablar), y se decidió que el resto de funcionalidades fueran enfrascadas, en un nuevo proyecto. U

Born of Triceratops and cF Studio

El proyecto cF comenzó como plataforma de comunicación y gestión de datos inalámbrica sobre micro-controladores de medio y bajo rango. Cuyo principal objetivo era crear una adaptación genérica y simple de microcontroladores de bajo coste al marco de telecomunicaciones contemporaneo, de manera ultra-eficiente aprovechando al máximo las “limitadas” características de los microcontroladores mid-range.

Un lenguaje de muy alto nivel escrito en c++ orientado a simplificar la interacción con el usuario.
No es orientado a objetos pero cuenta un dinámico sistema de controles programables e interpretados por el cliente.

A medida que se desarrollaba, y dada la excesiva “limitación” de muchos micro-controladores del mercado, surgió la opción de diseñar y crear un dispositivo capaz de abarcar todas las características de la plataforma.

El dispositivo, bautizado como Triceratops es un compendio de diversos micros, memorias, y entradas / salidas, fácimente programable via wifi o usb.

Se han creado varias librerías para diferentes modelos de micro-controladores con fínes didácticos. Y una más para el prototipo de Triceratops.

 La plataforma cF está conformada por el compilador cf Studio(Windows), y varios controladores para diferentes plataformas como Frog (Windows), y Mantis (Html).

Elementos integrantes de la plataforma.

A continuación

Name	Element	Status	Info	Developed in	Platform	Habitat
CF studio	CF Compiler	0.1	Edit and burn cf script.	C#	Windows	PC
	CF Memory	0.2	Wiew edit and burn hex files.	C#	Windows	PC
	CF Simulator	Early development	Cf Script simulator.	C#	Windows	PC
Rhino	Icon based scripting	Early development	Browser based remote burn and edit.	Javascript, html	Browser	PC, Adroid, Mac
Mantis	Process live control	0.2	Browser based conrol	Javarcript,html	Browser	PC, Adroid, Mac
Tuna	Process execution	1.12	Specific for each uC or device.	C/c++	See uC platform list	A uC chip.

# Features
Byte addressed.
Low memory usage architecture.
Low power consumption.
Dynamic communications.

# Needs
FRAM memory chip in order to make a larger PS
# IDE installation
Arduino version 1.6.5

Arduino > options > references, paste:

http://arduino.esp8266.com/versions/2.3.0/package_esp8266com_index.json

Find Esp8266 board version 2.3.0 in board manager.

A further explanation:

http://www.instructables.com/id/Programming-the-WeMos-Using-Arduino-SoftwareIDE/
# System io

Note: All pinouts references in this manual and libraries are focusing on Wemos D1R2,the bottom image, but some D1 board releases are printed as the image on top. This documentmust be interpreted as a Wemos D1R2 in pin map terms.

# Memory organization
## AUSR Absolute or static Setup registers
Memory organization for inuuc triceratops. The table below shows the Absolute Setup registers
We can see how AUSR is placed in the memory using memFM as the picture below.

## AURR Relative or dynamic Setup registers
The table below shows the relative registers. As its name defines them their length is relative to the user created script.

This is an instruction sector.
### VARIABLES sector (VAR)
Flash variables are storaged here, its length is dynamic. The first byte of the sector allocates the flash var amount (n), and the next n bytes are each variable's lengths in bytes, and next, variables in the same order.

In the picture above, the pink bytes are the VAR sector. The First 0x02 byte says there are two variables, the next 0x06 tells us that the first variable length in bytes is six, the next 0x04 tells us the length of the second and last variable. The following six bytes are the first variable, and the last four bytes are the second and last flash variable.

### SETUP sector (SET)

This sector's instruction width in bytes is 8. So the interpreter knows the instruction amount.
SET sector happens once each chip switch on, after connections are stablished.
We can see this sector marked as purple on the top image . It contains two instructions 'F100…' and 'F100…', in this case its setting some variable values.
This is an instruction sector.
### LOOP sector (LOO)
This sector's instruction width in bytes is 8. So the interpreter knows the instruction amount.
Every instruction in this sector happens each cycle, cycle length is stablished in tuna, default is 100ms.
This is an instruction sector.
### TIMER sector (TIM)
This sector's instruction width in bytes is 8. So the interpreter knows the instruction amount.
Every instruction in this sector happens each TIM cycle, cycle length is stablished in tuna, default is 1000ms.
This is an instruction sector.
Tickers are storaged here. After function indexing in workflow, so they must be declared out of any sector brackets.

### FUNCTIONS sector (FUN)
This is how the functions are indexed in Inuuc's flash memory.

The image shows part of the memory of a script shown by memFlashMap software.
Green coloured bytes are he fun sector.
First byte indicates the n (amount) of functions present in the script.
The next n bytes indicate the length each function.
A we can see in address 0x00 we have 3 functions, the first one's length is 1, and the 2nd and 3rd's length is 2.
And the first function from the stack starts in the fourth byte.

Max instructions in a function is 256.
Max functions in a script is 256.
Only functions accepted.
### EXTERNAL CONTROLS sector (CON)

### Names sector (TEX)
Tex sector stores elements names if needed, it is a character string.

The picture on top shows the TEX sector (when exist), it takes so much place in flash and its designed to use only when an external aplication will access the device's elements. Its not mandatory even in this case. If a variable is not indexed in the TEX sector its name will be shown as its hex name (F100, F202...).
The external aplication will interpret each element of the TEX sector by the following syntax:
<TYPE><HEX ADDRESS>:<NAME>;
Max value for Hex address is 0xFF and there is not a max limit for name lengths or name amount but its highly recomended to use them as less as possible and make them as short as possible.

### BUFFER sector (BUF)
 This sector is stored in RAM memory, it can be loaded and executed externally.
This sector has the highest priority in the execution thread.
It can be loaded by the serial root or via http

# Execution
## The life cycle of a script

The execution process of a script is directed by several pointers at “same time”. Mostly all sector have its own pointer, with some exceptions as functions where each function has its own pointer, and sectors like VAR and CON witch dont use pointer because are not interpreted as instructions.
Those pointers are, and TIM_POINTER
### TIM sector initialization and execution
Execution of TIM sector loop starts here. It will repeat the contents of TIM sector each 1000 ms (default).
The pointer is called TIMER_POINTER
### LOO sector initialization and execution
Execution of LOO sector loop starts here. It will repeat the contents of LOO sector each 100 ms (default).
The pointer is called LOOP_POINTER
### Communications initialization
Serial root starts listening.
In wifi provided device libraries such as triceratops, AP and LAN listeners are initialized previously.
### SET sector execution
The contets of SET sector will be executed once, and SETUP_POINTER will remain in the last position.
The pointer is called

# Board communications

Serial root: With a pc by usb cable
Optional ISC [Inuuc Serial Command] channels : with anoder microcontrollers.
Access point: Internet device, straight on.
Client mode: Internet device via Router or AP.

## Serial Root Communications.
Serial root is used to send commands and execute them in real time

Inuuc Serial root communications protocol is very simple, a packet involves two parts, the word and the control bytes.
The word its an 8 byte word containing an instruction.
The control bytes will tell the chip what to do with this instuction.
Frog compiler can send packets on runtime, those are get from lineGen via compilation.
Loading or triceratops.h is required, if the user wants to use Chip Register Constants.
Also if user wants to use compiler variables and functions, a program must be loaded on chip, with those elements properly declared.

Control word meanings:
- 0x00ZZ Store and execute instruction in BUFFER adress ZZ.(Enter key in cF console sends 0000).
- 0x01ZZ Store only in buffer adress ZZ.
  (Ctrl + NUM in cF console, for addresses 0-9).
- 0xFFFD Execute full buffer
- 0xFFFE	Clear buffer
- 0xFFFF	Print hex raw flash memory.(Used by dFrog)

### SRC priority

Root serial has the highest prority in all communications with the device.
This is stablished by bool ROOT_SERIAL_BUSY flag in tunacore.
If ROOT_SERIAL_BUSY=true; then sector LOO and TIM wont be read by the program polling pointers.
It must be re set to false after finishing the SRC communication, otherwise, device wont read any instruction.

## AP As Access Point

## LAN To a Local Area Network
# cFrog Programming
Advertences

- If a variable is declared in set or loo or var sector, chip must be reseted after flashwrite to the changes take efect.
- Cannot use g as function name. Because g. is used to call a global variable from inside a function.
- Call function can have only three parameters and literal must be less than 0x1000 set by tuna core's understandVariables.
- A function cannot be called @function
- The return value of function id 0xff (0xFFFF) cannot be used as another function's parameter because 0xFFFF means no parameter in tunacore's chip_call_function funcion. So max function amount is FE.
- A variable name cannot contain symbols as : = ; “ /

## cFrog Declaration Epoch Workflow
The workflow order is very important, it explains why some variable types can or not access another types depending where are declared.

### Import and index includes
Generates a table with function name and address
No dependencies
### Index stablishments
Generates a table with stablishment name and address
No dependencies
### Index definitions
Generates a table with defomotopm name and address
No dependencies
### Index flash vars
Generates a table with variable name and address
Dependencies: indexed definitions
### Index ram vars
Generates a table with function name and address
Dependencies: indexed definitions, indexed flash vars
### Index functions
Generates a table with function name and address
Dependencies:indexed definitions, indexed flash vars and indexed ram vars
### Index tickers
Generates a table with tickers name and address
Dependencies:indexed functions
### Index Sectors
Generates a table with sector contents
Dependencies:indexed definitions, indexed flash vars and indexed ram vars
###

## cFrog Compile Workflow
### Compile Program Stack PS [AURR]
Program stack length is relative, burn start address is 0, sectors are sorted like the declaration below.
        Dim HEX_PS As String = SECTOR_CON & SECTOR_TEX & SECTOR_SET & SECTOR_LOO & SECTOR_TIM & SECTOR_FUN & SECTOR_VAR

### Static geographic registers [AUSR]
Measure relative registers and set values to AUSR .
That means setting values of relative registers into the static registers.
Compiler gets flash sectors lengths and start points and and set them on its place of the flash memory set by #stablishment statements.
AUSR memory to index sectors length is 4 per flash sector, 28 bytes.
The compiler burns them all toghether.
Its burning start address is AUSR_SCONs, the address reserved for the start point of control sector due to the sector sorting. The line below shows how its created in cFrog.
 Dim HEX_GEO_AURR = SCONs & SCONe & STEXs & STEXe & SSETs & SSETe & SLOOs & SLOOe & STIMs & STIMe & SFUNs & SFUNe & SVARs & SVARe

### Static network registers [AUSR]
Mandatory, normally included in network.h
#stablish AP_SSID 'INUUC@D1'c;
#stablish AP_PASS '11111111'c;
#stablish LAN_SSID 'MOVISTAR_45E2'c;
#stablish LAN_PASS 'YCTkauEjquhhNUJqfXcJ'c;
#stablish MASK '192.168.1.1'i;
#stablish GATE '255.255.255.0'i;
#stablish IP '192.168.1.200'i;

### Generate Hex
Put all toghether.
# UDP protocol
Interpret the data is a different issue depending on the instruction we are working on.
Uv, udp1 and udp2 are the protocols used to manage all de data transactions between elements.

UnderstandPackets function ien tunacore
## Udp1

## Udp2

INS: Instruction
UM: Understand mode
TA: Target address
TIT :Target index type
TIA :Target index address
ST: Source type
SA: Source address
SIT: Source Index type
SIA: Index address
UM : understand mode
- UM 0: Literal asignation
- UM 1: Data reference asignation
UnderstandPackets will understand SI and TI as offsets to refer both the target and the source, to bring the pointer to the desired address in the memory.
In this case ST and SA will stablish the first item in the array.

This structure is used by
print 0000,0001 – UDP1
- Set flash F000 -UDP2
- Set ram F100 -UDP2
- set chip pin F200 writeAdr() -UDP1
- set chip pin mode F300 writeAdr() -UDP1
- Toggle bit F2FF
# UV protocol:Source types
UnderstandVariables function in tunacore
Source data address has 2 bytes
The first byte is the source type indicator and the second byte is the source index.
If Source indicator's value is less than SOURCE_INDICATOR_THRESHOLD, tunacore.cpp's understandVariables function will understand it as a literal.
So the available data types range in the system will be from SOURCE_INDICATOR_THRESHOLD to 0xFF.
Examples:
F100 : source type is ram variable F1, and source address: 0x00
F202 : source type is pin setup F2, and source address: 0x02

source type
<SOURCE_INDICATOR_THRESHOLD	Literal value
F0	Flash variable
F1	Ram variable
F2	Pin value variable.
F3	Pin setup variable
F4	Time stuff
F5	ADC
F6	Ultrasound
F7	TIMER COUNTS
F8	TIMER REPEATS
FF	Function result
FE Function parameter

## UV:Literal data threatment
UnderstandVariables function in tunacore
There are two ways to use literal data.
- As assignation
- As parameter

Upper table data taking 0x8000 as source indicator threshold.
Due to word width capacity each way has different limitations, if we are using it as parameter, this literal's value must be less than the Source Indicator Threshold, otherwise it will be interpreted as a reference by the chip.

## The source indicator threshold
The source indicator threshold its the limit where the chip will stop understanding the data as literal from where it will start understanding the data as a source indicator in 2 byte data packets.
All functions ,maths and ifs params are affected by the SIT.

## F6 Ultrasound module

Warning: U HC-sr04 ultrasound module pins must be connected before the program starts otherwise chip will hang.

## FF Function result

  String FUNCTIONS_RESULTS[FUNCTIONS_MAX_COUNT];
## FE Function parameter
  String FUNCTIONS_PARAMS[FUNCTIONS_MAX_COUNT][FUNCTIONS_MAX_PARAMS];
The first index, functionIndex, must be get from functionIndex inside tuna, because the address FEXX can olnly send one address, XX is the parameter index.
Thats why they can only be used within a function.
## cFrog elements
### sectors

var(){
}
set(){
}
loo(){
}
tim(){
}
fun(){
}
con(){
}·

### #include
Includes work as usual c++
.h libraries contain tunacore register addresses with human names, to make easier to reference and use.
#include <triceratops.h>
### #define
Defines are always hex

Definition
#define A0 Faa0;

Read
ram a =A0;

### #stablish
  Its the way to set AUSR registers addresses, it tells the compiler where are the statics registers on chip. They store data as ssid , sector coords e t c .

Definition
#stablish sSETd 213123;

Read
ram a =A0;

### Variables
Assignations work in the same way for both fla and ram variables.
During compilation its possible to cross assing variables from fla to ram but not from ram to fla. This is due to the workflow sorting, see “cFrog compilation workflow”.
Variable data can be addressed in two ways:
- & symbol suffix gets variable address.
- $ symbol suffix gets variable value.

Flash variables
Must be declared inside VAR sector , type must be defined always, there is no space limitation.
Flash cannot get a ram value on declare epoch.
#define AA FEFE; // Define
var(){
hex A =AA; // value from definition
hex B ='FFFE'; // value from hex lit
dec C ='1234'; // value from dec lit
cha D ='Hello!'; // value from cha lit
hex E =$A; // value from A content
hex F =&A; // value from A address
}·
Ram variables
They can be declared on the header (between includes and set() sector), compiler will put them at the top of set() sector .
Ram variables can be declared in the sectors below

set()
loo()
tim()
fun() <- inside a function

 Literal data entry limit is 2 byte.
Ram can get Flash values on decllare epoch

#define AA FEFE; // Define
ram a =AA; // value from definition
ram dec b ='1234'; // value from dec lit
ram hex c ='ABCD'; // value from hex lit
ram cha d ='ON'; // value from cha lit
ram e =$a; // flash a content to e
ram f =&a; // flash a address to f

 Ram arrays
Ram arrays have some limitations, they can be declared only in D epoch.

&oak[COUNT] wont be accesible from ram a[] because of the index workflow
tic oak 0 counter.on(1,20)do @elm;
ram a[5] =(1),(&oak[COUNT]),(3);

Ticker is indexed after function because it is function dependant, function is indexed after ram variables because it is ram dependant.
So in this indexing order user cant reference a ticker from a ram array because the arrays must be declared on D epoch and no rams from D epoch can access to tickers references.

Oak
### Functions

Functions work similar to c++,
All function must be declared in fun() sector.
Functions have no parameters.
Its possible to declare variables and set values within a function, if a variable is declared within a function this can be used from any sector. See cFrog Declaration Epoch Workflow.
Its possible to call a function from a function. But the called one must be declared first, otherwise compiler will drop errors.
The @ suffix is neccesary to call a function, functions can be called from set(), loo(), tim(), fun() sectors
set(){
@oak();
}·
fun(){
@void elm(){
printf('1234');
}
@void oak(){
ram hex b ='FE';
if('a'==$b) do @elm();
}
}·

### Functions with Parameters
How it works
As we know, the function sector is filled by innerFunction sectors, witch are like a sector for each function, witch will be read by pointer.

The including of parameters in cF code means “tricking” frog assembler code because it has no way to directly get paramaters due to the reason explained in the previous paragraph.
cF code
@void pine(par0){
println(par0,CHA);
}

Frog assembler code

#set(F1…) // set par0 in ram in Declaration epoch

#fun(pine,0000F1AA….) // print F1AA, being F1AA the par0's address
cF code the alternative, old way, params with no params
ram par0 ='OK'c;
@void pine(){
println(par0,CHA);
}

Here we can see how the trick does work.

### Functions with Return

Set(){
@oak('HI'c);
ram a =@oak;
}
The function mus be called before retrieving the value, otherwise it will get the values from the previous function call.
A will get oak functions result from String FUNCTIONS_RESULTS[FUNCTIONS_MAX_COUNT]; in tunacore

### Conditions

The if statement has no else in frog 1.1

The output must be a previously declared function or a datatipe.

Today, IF statement output data types available are F0 and F1.
TODO: add the missing datatypes in tunacore.cpp around line 1061
function: chip_if_statement(String line,int statement)

if('a'==$b) do @elm(); // Calls elm function if true
if('a'==$b) do &b; // Stores result in variable b

It can be used in the sectors set(),loo() ,tim() and in fun(). In fun(), it must be inside a function.

### Mathematics operations ma()

Every result is stored as hexadecimal string.
If the result is floating it will be as a floating hexadecimal string.

Dec result = 11.01
Hex storage = B.01

The operations are listed below

ma(1.2)to &a;// decimal number to a variable
ma(10+&a)to &a;
ma(!&b)to &b; // toggle bit
ma(!&b)to &b; // toggle byte
ma(&b<<1)to &b;
ma(&b%1)to &b;
ma(!PD4)to 'F202'x;// toggle a pin
ma(!PD4)to PD4; // toggle a pin
ma(0.5)to &a; // floating trick same as bottom
ma(1/2)to &a; // same as top

### Data addressing wl(), wr() and ra()

Write in register address wl() and wr()
The functions wl() and wr() are used to write data into registers
the difference between both is that wl() will understand the source as literal and wr() will understand the source as reference.
wl(TD0,OUTPUT); // second parameter is interpreted as literal

wr(TD0,TD2); // second parameter is interpreted as reference

Read register adress ra()
The is the source address, so must be hex, and a valid address. Very useful to read pin values etc.
ram c=ra('F403');
ram d=ra(PIN_LED_VALUE);
ram d =ra($a); // use value of a to reference address
ram e =ra(&a); // use reference of a to reference address

### Digital IO statements

Reading and writing and setting up digital pins involves F2 (pin setup) and F3 (pin value) source types. Use wl() wr() functions to set pin status and pin value.
Pin status registers definitions are TD0 – TD0 in triceratops.h and pin values registers definitions are PD0 – PD0 in triceratops.h.
Value of the pin must be boolean.

wl(TD0,OUTPUT); // second parameter is interpreted as literal
wr(TD0,TD2); // second parameter is interpreted as reference
wr('F204',TD2); // first parameter is always as reference F2xx F3xx are writable
wl(TD0,&ON); // second parameter is interpreted as literal

### Tickers
tic pine 1 datetime.on(2018,01,01,20,02,01)do @elm;
tic oak 0 counter.on(10,1000)do @elm;

<declaration><name><status><type>.on(<params>)do <output>
tic pine 1 datetime.on(2018,02,12,13,30,01)do @elm;

tic oak 0 counter.on(1,20)do @elm;

Those only for counter¿?¿?¿
println(&oak[COUNT],0);
println(&oak[REPEATS],0);
same as
println(&oak['F7'x],0);
println(&oak['F8'x],0);

Control
 tic.enable(oak);
tic.disable(oak);

# Hypertext transfer protocol communications
Back end. Rhino, mantis and frog use this feature constantly.
During the compilation, UI and monitoring.
 Chip can be reached either by the access point or via LAN. But it has been probed that via LAN will work faster using a common router.

d_r_ee Read eeprom by decimal coords
This will return the specified memory bytes.
Structure
host//d_r_ee/&START_ADDRESS,BYTE_LENGTH
Example
92.168.1.200:81/d_r_ee/&0,4
Output
AABBCCDD (if the first four bytes have these value).
Notes
All in are DEC. All out are HEX. memFlashMap uses it.

d_r_ee Write eeprom by decimal coords
This will return the specified memory bytes.
Structure
host//d_r_ee/&START_ADDRESS,BYTE1,BYTE2,BYTEn
Example
http://192.168.1.200:81/d_w_ee/&0,1,2,3,4
Output
{"row":[{"result":"OK","bytes":"4"}]}
Notes
All in are DEC. All out are HEX. Output:

x_w_ee Write eeprom by hexadecimal coords
This will return the specified memory bytes.
Structure
host/x_w_ee/&START_ADDRESS,BYTE1BYTE2BYTEn
Example
http://192.168.1.200:81/x_w_ee/&0,0A0B0C0D
Output
{"row":[{"result":"OK","bytes":"4"}]}
Notes
MemEdit uses is to record program. / cF uses is to record program.

d_c_ee Clear eeprom by decimal coords
This will return the specified memory bytes.
Structure
host/d_c_ee/&START_ADDRESS,LENGTH_IN_BYTES,CLEAR_SYMBOL
Example
http://192.168.1.200:81/d_c_ee/&0,4096,0
Output
{"row":[{"result":"OK","bytes":"4096"}]} / Clears full flash.
Notes
cF uses it to clear eeprom on program burn.

# Instructions, controls and declarations

Rhino gives all code to frog, there are some parts of the code witch are precompiled by rhino as the TEXTS of the elements (controls vars etc).

## Instruction dictionary

0000 Chip print value				0000
This will print the value in the hyperterminal, for technical usage only. The previous word will print the variable flash adressed 0x00 in the monitor.
Instruction syntax
A	B	C	D	E	F	G	H
00	00	F0	00	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Understand Mode
D	Target Address
E	Literal / Free
F	Literal / Free
G	Literal / Source Indicator
H	Literal / Source Address
Rhino
	Drop this element to a non declaration sector.

Stored via Understand Input Packets

[FFXX] Call function				FF00
This will call a function previously declared in the FUNCTION sector.
Instruction syntax
A	B	C	D	E	F	G	H
FF	12	ff	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Function address
C	Param 0 source indicator
D	Param 0 source address
E	Param 1 source indicator
F	Param 1 source address
G	Param 2 source indicator
H	Param 2 source address
Rhino
	Drop this element to a non declaration sector.

C to H bytes 0xFFFF as parameter value means no parameter.
Last edit 020218

FE00 Set function local variable				FE00
This is a return of a funcion, it stores the data via understand variables.
Instruction syntax
A	B	C	D	E	F	G	H
FE	02	00	00	00	FF	FF	FF
Keys
A	Instruction
B	Function address
C	Data type
D	Data address
E	Local variable address address
F	Unused / literal
G	Unused / literal
H	Unused / literal
Rhino
	Not present

This instruction has a parametric Literal input: If literal is higher than SOURCE_INDICATOR_THRESHOLD it wont be understood as literal, but as reference.
Last edit 030218

0002 Set function result slot				0002
This is a return of a funcion, it stores the data via understand variables.
Instruction syntax
A	B	C	D	E	F	G	H
00	02	00	00	00	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Understand Mode
D	Target Address
E	Literal / Free
F	Literal / Free
G	Literal / Source Indicator
H	Literal / Source Address
Rhino
	Not present

This instruction has a parametric Literal input: If literal is higher than SOURCE_INDICATOR_THRESHOLD it wont be understood as literal, but as reference.
Last edit 030218
Stored via Understand Input Packets????

F400 Set chip time				F400
This will set compile time or it will get time from server and set it as main date time on the chip. Some features require an internet connection.
Instruction syntax
A	B	C	D	E	F	G	H
F4	00	00	10	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Source
D	Timezone
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

Source 0x00 : inuuc server

F200 Set chip pin value				F200
This will stablish a pin setup as INPUT or OUTPUT. 0 is input.
Instruction syntax
A	B	C	D	E	F	G	H
F2	00	00	00	02	00	FF	FF
Keys
A	Instruction
B	Instruction
C	Understand Mode
D	Target Address
E	Literal / Free
F	Literal / Free
G	Literal / Source Indicator
H	Literal / Source Address
Rhino
	Drop this element to a non declaration sector.

Notes: if final the value is not 1, result will be 0. only if its 1 will be one.

Stored via Understand Input Packets

F300 Set chip pin setup				F300
This will stablish a pin setup as HIGH or LOW. 0 is input.
Instruction syntax
A	B	C	D	E	F	G	H
F3	00	00	00	02	01	FF	FF
Keys
A	Instruction
B	Instruction
C	Understand Mode
D	Target Address
E	Literal / Free
F	Literal / Free
G	Literal / Source Indicator
H	Literal / Source Address
Rhino
	Drop this element to a non declaration sector.

Via Understand input packet

F2FF : Toggle chip pin value				F2FF
This will toggle a pin value.
Instruction syntax
A	B	C	D	E	F	G	H
F3	FF	00	00	02	01	FF	FF
Keys
A	Instruction
B	Instruction
C	Unused *
D	Bit Address
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

F000 Set FLASH variable value				F000
This will set a value to a PREVIOUSLY DEFINED flash variable.
Instruction syntax
A	B	C	D	E	F	G	H
F0	00	00	00	02	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Understand Mode
D	Target Address
E	Literal / Free
F	Literal / Free
G	Literal / Source Indicator
H	Literal / Source Address
Rhino
	Drop this element to a non declaration sector.

Stored via udp1

[F100] Set RAM variable value				F100
This will set a value to a ram variable. Ram variables are not declared, name, if its, will be token from the first data set on the variable.
Instruction syntax
A	B	C	D	E	F	G	H
F1	00	F0	41	02	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Understand Mode 0 literal 1 reference
D	Target Address
E	Literal / Free
F	Literal / Free
G	Literal / Source Indicator
H	Literal / Source Address
Rhino
	Drop this element to a non declaration sector.

Stored via up1

[A0] Set Flash, literal value				A0
It will set a literal value using udp2 protocol, but TIT and TIA bytes will be ignored because there are no arryis in flash
Instruction syntax
A	B	C	D	E	F	G	H
A0	00	00	00	00	FF	FF	FF
Keys
A	Instruction
B	Target Address
C	Target Index Type Unused
D	Target Index Address Unused
E	Literal
F	Literal
G	Literal
H	Literal
Rhino
	Drop this element to a non declaration sector.

up2

[B0] Set Flash, reference value				B0
It will set a reference value value using udp2 protocol, but TIT and TIA bytes will be ignored because there are no arryis in flash. / Source will include source index and source, 4 bytes
Instruction syntax
A	B	C	D	E	F	G	H
B0	00	00	00	00	FF	FF	FF
Keys
A	Instruction
B	Target Address
C	Target Index Type Unused
D	Target Index Address Unused
E	Source Index Type [SIT]
F	Source Index Address [SIA]
G	Source Type [ST]
H	Source Address [SA]
Rhino
	Drop this element to a non declaration sector.

Stored via up2

[A1] Set Ram, literal value				A1
It will set a literal value using udp2 protocol, as every ram variable is an array TIT and TIA bytes are used.
Instruction syntax
A	B	C	D	E	F	G	H
A1	F1	01	00	00	FF	FF	FF
Keys
A	Instruction
B	Target Address
C	Target Index Type [TIT]
D	Target Index Address [TIA]
E	Literal
F	Literal
G	Literal
H	Literal
Rhino
	Drop this element to a non declaration sector.

[B1] Set Ram, reference value				B1
It will set a literal value using udp2 protocol, as every ram variable is an array TIT and TIA bytes are used.
Instruction syntax
A	B	C	D	E	F	G	H
B0	00	00	00	00	FF	FF	FF
Keys
A	Instruction
B	Target Address
C	Target Index Type [TIT]
D	Target Index Address [TIA]
E	Source Index Type [SIT]
F	Source Index Address [SIA]
G	Source Type [ST]
H	Source Address [SA]
Rhino
	Drop this element to a non declaration sector.

Stored via Understand Input Packets

[E0][D1] Date time related if statement				[E0][D0]
This is a timer, it will trigger the stablised function on the stablished date-time coincidence with the CHIP MASTER TIME.
Instruction syntax
A	B	C	D	E	F	G	H
EE	0B	03	22	05	36	00	00
Keys
A	Instruction
B	Year YY
C	Moth MM
D	Day DD
E	Hour HH24
F	Minute MM
G	Second SS
H	Output function
Rhino
	Drop any of those elements to TIMER or LOOP sector.

[E1][D1] Countdown related if statement					[E1][D1]
This is a timer, it will trigger the stablised function after the stablished period has transcurred, loops are allowed. The following example will trigger the function 0x00 each minute, forever.
Instruction syntax
A	B		C	D	E	F	G	H
EF	0B		00	00	00	00	3C	00
Keys
A	Instruction
B	REPEATS R1 [0=forever]
C	REPEATS R0 [0=forever]
D	COUNT C3
E	COUNT C2
F	COUNT C1
G	COUNT C0
H	Output function
Rhino
		Drop any of those elements to TIMER or LOOP sector.

[0003] Enable / disable ticker				0003
This this will enable or disable ANY TYPE of timer
Instruction syntax
A	B	C	D	E	F	G	H
ED	FF	00	01	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Action: ENABLE / DISABLE
D	Timer address
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

[0004]Reset ticker count				0004
This this will reset ANY TYPE of timer
Instruction syntax
A	B	C	D	E	F	G	H
ED	FE	00	01	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Action: ENABLE / DISABLE / DO NOTHING
D	Timer address
E	Reset action : COUNT / REPEATS / DO NOTHING
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

[0007] Re run setup				0007
Used as dev.rst() from cF it runs setup again. This instruction has no arguments.
Instruction syntax
A	B	C	D	E	F	G	H
00	07	FF	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Unused
D	Unused
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Not present

[0005] Skip line forward				0005
Used as skip(1) from cF as instruction as OH element. Parameter must be decimal.
Instruction syntax
A	B	C	D	E	F	G	H
00	05	FF	FF	FF	FF	FF	01
Keys
A	Instruction
B	Instruction
C	Unused
D	Unused
E	Unused
F	Unused
G	Unused
H	Skip lines positive count.
Rhino
	Not present

[0006] Skip line backward				0006
Used as skip(-1) from cF as instruction as OH element. Parameter must be a negative decimal(Otherwise tuna will execute 0005 instruction).
Instruction syntax
A	B	C	D	E	F	G	H
00	06	FF	FF	FF	FF	FF	01
Keys
A	Instruction
B	Instruction
C	Unused
D	Unused
E	Unused
F	Unused
G	Unused
H	Skip lines negative count.
Rhino
	Not present

On change statement				2F00
This will trigger a function when a value changes and complies with the stablished conditions
Instruction syntax
A	B	C	D	E	F	G	H
ED	FE	F4	08	00	FF	FF	00
Keys
A	Instruction
B	Instruction
C	Source data type
D	Source address
E	On change mode: CHANGE / INCREMENT / DECREMENT
F	Unused
G	Output function type
H	Output function address
Rhino
	Drop this element to a non declaration sector.

[010X] If statements				010X
This will trigger a function when a comparation complies with the stablished conditions. / Or it will return a TRUE FALSE value of the comparation.
Instruction syntax
A	B	C	D	E	F	G	H
ED	FE	00	08	00	FF	FF	00
Keys
A	Instruction
B	If statement type
C	A Source data type
D	A Source address
E	B Source data type
F	B Source address
G	Output type
H	Output address
Rhino
	A equals B, only non declaration sectors, hex mnemonic is 0x00.
	A not equal B, only non declaration sectors, hex mnemonic is 0x01.
	A greater than B, only non declaration sectors, hex mnemonic is 0x02.
	A not greater than B, only non declaration sectors, hex mnemonic is 0x03.
	A less than B, only non declaration sectors, hex mnemonic is 0x04.
	A not less than B, only non declaration sectors, hex mnemonic is 0x05.

[011X] Maths operations				011X
This will return the algorithmic resultant value of the stablished operation and values.
Instruction syntax
A	B	C	D	E	F	G	H
01	10	F1	00	F1	01	F1	02
Keys
A	Instruction
B	Operation
C	A Source data type
D	A Source address
E	B Source data type
F	B Source address
G	Output data type
H	Output address
Rhino
	Add
	Substract
	Multiply
	Divide
	Shift left
	Shift Right
	And
	Or
	Not
	LSB not

Transmit chip status				B000
TO DO
Instruction syntax
A	B	C	D	E	F	G	H
C0	00	00	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Log slot address
D	Log slot item index * [not implemented yet]
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

Serial command to channel				B1XX
Reads a child clip via wire.
Instruction syntax
A	B	C	D	E	F	G	H
B1	00	00	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Channel
C	Inuuc Serial Command A byte
D	Inuuc Serial Command B byte
E	Inuuc Serial Command C byte
F	Inuuc Serial Command D byte
G	Response storage data type
H	Response storage data address
Rhino
	Drop this element to a non declaration sector.

See table 7.4.2 to find the Inuuc Serial Command list.

Response will be storaged in the G and H set memory slot.

Serial handshake to channel				B2XX
Reads a child clip via wire.
Instruction syntax
A	B	C	D	E	F	G	H
B2	00	00	FF	FF	00	FF	01
Keys
A	Instruction
B	Channel
C	If true function
D	If false function
E	Void
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

See topic 7 for Inuuc Serial Commands information.

A Function

Serial channel init				B3XX
Reads a child clip via wire.
Instruction syntax
A	B	C	D	E	F	G	H
B2	00	00	FF	FF	00	FF	01
Keys
A	Instruction
B	Channel
C	Unused
D	Unused
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

See topic 7 for Inuuc Serial Commands information.

A Function

Clear log slot				C000
This clears a log slot on the selected chip.
Instruction syntax
A	B	C	D	E	F	G	H
C0	00	00	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Log slot address
D	Log slot item index * [not implemented yet]
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

Add to log slot				C001
This clears a log slot on the selected chip.
Instruction syntax
A	B	C	D	E	F	G	H
C0	01	00	00	FF	FF	F1	00
Keys
A	Instruction
B	Instruction
C	Log slot address
D	Log slot item index
E	Unused
F	Unused
G	Source data type
H	Source data address
Rhino
	Drop this element to a non declaration sector.

## Declarations

Flash var declaration		VAR
This allocates flash memory on chip and builds a content index.
Declaration syntax
Type	CHAR*, IPA, DEC, HEX
Value	Any Integer
Rhino
	Drop this element to VAR sector only.

* Char will dissapear.

Function declaration		FUN
This allocates flash memory on chip and builds a content index for a function. A new sector box will be built in rhino, to add instructions to the function. By another hand, in Frog, instructions must be add by separating them by dots.
Declaration syntax
Address	Read only, set by the sorting of declarations.
Content	Any Instructiond dropped to each function sector.
Rhino
	Drop this element to FUN sector only.

* Char will disappear

## Live control dictionary

Pin control				C000
This returns all selected pin setup and value
Instruction syntax
A	B	C	D	E	F	G	H
C0	00	00	00	FF	FF	F1	00
Keys
A	Instruction
B	Instruction
C	Select IO to show by 24 bit (lsb 17 used) binary string, only used in show selected mode.
D
E
F	Select IO to show mode INPUTS / OPUTPUTS / ALL / SELECTED
G	Select buttons to show UPDATE / SAVE / NONE / BOTH
H	Select textboxes to show VALUE / SETUP / BOTH
Rhino
	Drop this element to the CONTROL sector only.

Show value				C001
This returns all selected pin setup and value
Instruction syntax
A	B	C	D	E	F	G	H
C0	01	00	00	FF	FF	F1	00
Keys
A	Instruction
B	Instruction
C	If (data type = F0) / {ReadAs :Variable data type, says how its gonna be interpreted if read, CHA, DEC, HEX or IPA.}
D	Select buttons to show UPDATE / SAVE / NONE / BOTH
E	Source data type
F	Source address
G	Unused
H	Unused
Rhino
	Drop this element to the CONTROL sector only.

Call function				C002
This executes the specified function.
Instruction syntax
A	B	C	D	E	F	G	H
FF	00	00	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Function address
D	Unused
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to a non declaration sector.

All data type select				C003
This returns a dropdown making visible any of the values stored on chip.
Instruction syntax
A	B	C	D	E	F	G	H
C0	03	FF	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Unused
D	Unused
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to the CONTROL sector only.

IO box				C004
This builds IO control box.
Instruction syntax
A	B	C	D	E	F	G	H
C0	04	00	00	02	03	03	02
Keys
A	Instruction
B	Instruction
C	Select IO to show by 24 bit (lsb 17 used) binary string, only used in show selected mode.
D
E
F	Show mode select INPUTS / OUTPUTS / ALL / SELECTED
G0	Orientation VERTICAL / HORIZONTAL
G1	Width 1 : 12
H0	Show buttons UPDATE / SAVE / NONE
H1	Show pin VALUE / SETUP
Rhino
	Drop this element to the CONTROL sector only.

Logger				C005
This logs the stablished values each stablished cycle, it optionally generates a chart. On some chart slot 0 will be the X edge of the chart.
Instruction syntax
A	B	C	D	E	F	G	H
C0	05	FF	FF	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Log slot address
D	Period in cycles
E
F	Slot item 1:F
G	Unused
H0	Chart type
H1	Chart size
Rhino
	Drop this element to the CONTROL sector only.

Cam streaming frame				C006
This builds a frame invoking the assigned ip camera, ip and port address and sufix must be stored in a FLASH variable as hex.
Instruction syntax
A	B	C	D	E	F	G	H
C0	06	00	01	FF	FF	FF	FF
Keys
A	Instruction
B	Instruction
C	Source url params as FLASH address
D	Source suffix param as FLASH address
E	Unused
F	Unused
G	Unused
H	Unused
Rhino
	Drop this element to the CONTROL sector only.

# Inuuc Internal Serial Communications
## Overview
Its going to be used when add on modules will be implemented.
Some modules are CMOS and others TTL, there is a tension divider option to solve this.
This is not needed for D1 – D1 communications but required for arduino Uno or 168 based boards.
## Serial channels
There are two serial channels useable in inuuc, channel uses pins D1 and D2, and the channel 1, D5 and D6.
Channel	Pin	Function
ss0	D1	Rx
	D2	Tx
ss1	D6	Rx
	D7	Tx

## Serial Slave Handshake
The handshake happens when slave receives 4 0xFF in a row and answers with an @ ascii 64.
Then the byteSYNC register will reach 4 value and ByteID register will be reseted to 0 value, getting the slave ready for receive.

## Serial Slave Send word

Send word function will send a 4 byte word and get the one byte answer from slave in selected channel.
Its hardly recomended to set the handshake flag as “true”, the master will do a handshake each word.

### Serial Slave Sending words: the comm function
ssm.comm(0,0xF2,0x00, 0x02, 0x01,true);
ssm.comm(channel, a ,b, c, d, handshakeFlag);
if called commands result is void answer must be 41, else answer must be the asked result.
If the result is -1 there is a communication error. Be sure you call init(…), baudrate, and check if device is properly wired.
### Send word Commands
	rxWord[0]	rxWord[1]	rxWord[2]	rxWord[3]
Digital setup	F2	00	INT pin	BOOL value
Digital value	F3	00	INT pin	BOOL value
Digital read	F3	FE	INT pin	NOT USED
Analog read [2]	F5	00	INT pin	INT msb or lsb
Analog write PWM [1]	F5	FF	INT pin	INT PWM duty

# Notes
1. Atmega 168 PWM works on pins 3, 5, 6, 9, 10, and 11.  The frequency of the PWM signal on most pins is approximately 490 Hz. On the Uno and similar boards, pins 5 and 6 have a frequency of approximately 980 Hz.
  https://www.arduino.cc/reference/en/language/functions/analog-io/analogwrite/
2. Analog read takes about 100 microseconds (0.0001 s) to read an analog input, so the maximum reading rate is about 10,000 times a second.
  https://www.arduino.cc/reference/en/language/functions/analog-io/analogread/